;REBOOT in dos mode

;mode com2:96,n,8,1

;set directory path

;type clearram.txt>com2:

;type rocksub.mot>com2:

;

;

;memory assignments			P2

;reset vector, interupt routines		p3

;main program loop			p4

;subroutines:-

;Volts					p5

;Sideon					p6

;seconds					p6

;   Revs					p6-7

;   Starter				p7

;   Sdelay				P7

;   Minute				P8

;Sidecnt, stall				p9-10

;getkey					p11

;Keys					p12-19

;   Runkeys				p12

;   Digit				p13

;   RCLs					p13-14

;   Numin				P15

;   Key Processors			P16-19

;	A-C				P16

;	D				P17-18

;	*				P18

;	#				P19

;	Nokey				P19

;LRCntdp					P20

;Unlock					p20-22

;Initky					P22

;Initdp					P22

;Clrdp					p22

;Dispdat					p23

;LCD					p23

;Scankbd					p24-25

;Displ					P25

;Delay					p25

;Numchr					p26-27

;Inital					p27-29

;Strings					P29

PORTA	EQU	$00	[0,1] = LCD CNTRL [2.5] LCD DATA

PORTB	EQU	$01	Outputs

PORTC	EQU	$02	Keyboard Rows[4-7], LCD Data[0-7]

PORTD	EQU	$03	A/d, I2

DDRA	EQU	$04

DDRB	EQU	$05

DDRC	EQU	$06

TIMDAT	EQU	$08	Timer Rgstr set for 10ms

TIMCTL	EQU	$09	Timer control

MRI2	EQU	$0A	I2 register

ADCTL	EQU	$0E	AD control

ADDAT	EQU	$0F	A/D Data

REVCNT	EQU	$10	Revs register not cntr		PortB bits

MODE	EQU	$11	Mode bits			0 Led

MAXREV	EQU	$12	Maximum Rev count		1 Not used

MINTIM	EQU	$13	Min side timer			2 water

MINCNT	EQU	$14	counter for minutes		3 blade

SECS	EQU	$15	counter for seconds		4 reciprocate

DEBNCE	EQU	$16	debounce timer			5 auxilary

OLDKEY	EQU	$17	last key pressed			6 left

K	EQU	$18	Current key			7 right

WATERST	EQU	$19 	Water start timer

ENTRYM	EQU	$1A	Current keyboard mode

CNTH	EQU	$1B	count bytes low/high

CNTL	EQU	$1C	for kybrd input of nums

TEMPL	EQU	$1D	used for decoding lrcnt

TEMPH	EQU	$1E	to characters for diply

LRCNTH	EQU	$1F	Left/Right Counter			Display map

LRCNTL	EQU	$20	counts down to zero		   0123456789abcdef

CC	EQU	$21	Char Cnt to convert		40 Txx-xx Rxxx Vxxx

NUML	EQU	$22	Number for conversion		50 Lxxxx-xxxx mode

NUMH	EQU	$23	to characters

MR	EQU	$25	misc reg (high byte A)		mode(bits)

CNTDWN	EQU	$26	Timer count down			0

LOCKED	EQU	$27	Lock status			1

BLADEST	EQU	$28	Blade start timer		2

OLDEM	EQU	$29	old entrymode			3

SIDE	EQU	$2A	side move status			4 Countdown

TSS	EQU	$2B	Side Start timer			5 Norm/grind

OLDLR	EQU	$2C	Old side move status		6

MAXV	EQU	$2D	Maximum Volts			Entrymode(number)

LRTIM	EQU	$2E	Left/Right Tmr for stall	0 		Nil

REVCT	EQU	$2F	Rev counter (interupt)			1 Timer

UPCNT	EQU	$30	countdown timer				2 Left

LRRATE	EQU	$31	Side Shift speed				3 Right

LRDELY	EQU	$32	Side Shift speed counter			4 Double

ONTIME	EQU	$33

TLRON	EQU	$34	Water counter				Side(bits)

MINIDL	EQU	$35	Minimum idle count 			0 Right

FREE4	EQU	$36						1 Left

CHRD	EQU	$37	Character to display			2 Start

VOLT	EQU	$38	Current voltage

OLDW	EQU	$39	Old Water status

MSGPTR	EQU	$3A	message pointer

MSGPTR2	EQU	$3B

LRHOLD	EQU	$3C	key holdon timer

NOKHOLD	EQU	$3D	nokey pressed timer

DPTR 	EQU	$3E	where to place chrd in display reg

LCDPTR	EQU	$3F	LCD ptr

LRLOLD	EQU	$61

LRHOLD	EQU	$62

ORG	$0FF8

FDB	I2		SET START, RESET, INTERUPT POINTERS

FDB	INT

FDB	I2

FDB	MAIN

ORG	$100		Stop Bar interupt, when it hits the rock

I2	SEI			STOPS MACHINE

LDA	#$01		$FFA,$FFB

STA	PORTB		Turn off all.

LDA	#$59

STA	DPTR

LDA	#7

LDX	#STOPBR-#$0C00

JSR	DISPL

CLR	MODE

LDA	#$0F

STA	LOCKED		Lock machine

LDA	#$70		Enable only lowest row

STA	PORTC		of keyboard

LOCK	BRSET	5,PORTA,LOCK	Loop until "D" typed

LDA	#$04

STA	DEBNCE		Debounce time = 40ms

LDA	#$0D

STA	OLDKEY

CLR	MRI2

JSR	INITKY

RTI

;(*******************)

;Increments revcounter on each interupt, generated by three magnets on

;blade pully

INT	INC	REVCT		Increment rev counter

RTI

;Main program and 10ms loop

MAIN	LDA	#$0F		This is the main program

STA	LOCKED

JSR	INITAL

LDX	#$40

JSR	CLRDP		clear display register

JSR	INITKY		set display for first unlock key

IDLE	LDA	TIMDAT		establish minimum cpu idle time

CMP	MINIDL		in following loop

BHI	IDLE2

STA	MINIDL

IDLE2	LDA	TIMDAT		wait until timer times out (10ms)

BNE	IDLE2

JSR	LCD		display next character from display reg

CLR	ADCTL		AD0 TO CONVERT

LDA	#126		78 PER 10 milliseconds

STA	TIMDAT

JSR	GETKEY		get next key

JSR	KEYS		process keys

TST	LOCKED

BNE	IDLE		Machine locked? - return to idle

JSR	VOLTS		Update voltage, and check for overload

JSR	SIDEON		Check sideshift ON time

JSR	SIDECNT		count sideshift if active

DEC	SECS

BNE	IDLE

JSR	SECONDS		update second counter, and do 1hz stuff

DEC	MINCNT		decrement minute counter every second

BNE	IDLE		and do minute stuff if 1 minute

JSR	MINUTE

BRA	IDLE		loop back

; Subroutines

;Gets voltage from A to D, establish maxV, check for overload

;(Yallorn to Rocksaw has close to 1 ohm series resistance)

;turns led on when close to overload

VOLTS	LDA	ADDAT		VOLTS - done every 10ms, read A/D converter

CMP	VOLT		Get volts, has it changed from last sample?

BEQ	RTNVLT		No - return from sub

STA	VOLT		Yes - update volt, and place value in X reg

TAX

LDA	#$4D		set display ptr to character position

STA	DPTR            for voltage

CLR	MR		place high byte (in this case 0) into MR

LDA	#$03		set number of chrs to convert

JSR	NUM_CHR		gosub number to character converter

L13	TST	BLADEST		Blade starting flag

BNE	RTNVLT		Is machine Starting? - Yes - return

BRCLR	2,PORTB,NMAXV	If water is off it affects V, skip maxvolt

TST	WATERST		Has water been turned on in last 2 secs?

BNE	RTNVLT		If so, impulse causes low volts -skip

LDA	VOLT		No to above, then volt reading OK

CMP	MAXV		Is Volt > maxV

BLS	NMAXV

STA	MAXV		Yes - then MaxV = Volt

NMAXV	BRCLR	3,PORTB,RTNVLT	Is Blade running? No - return

LDA	MAXV

BRSET	4,PORTB,CDM2	Is Mode = timer (ie unattended)?

SUB	#08		No - then attended - allow extra 8v (~8A)

CDM2	SUB	#13

CMP	VOLT		Is Volt < MaxV - 13(21)v

BHI	LEDONV		Yes - then Led On

BSET	0,PORTB		No - then Led off

RTNVLT	RTS

LEDONV	BCLR	0,PORTB		turn led on

SUB	#09		Is Voltage < MaxV - 22(30)v

CMP	VOLT

BLS	RTNVLT		No - return

LDA	#$01		Yes - Turn machine off

STA	PORTB

LDA	#$20

LDA	#$59

STA	DPTR

LDA	#7

LDX	#LOVOLT-#$0C00

JSR	DISPL

LDA	#$0F

STA	LOCKED		Lock Machine

RTS

;Side shift stall check - Decrements side shift ON time counter (every 10ms)

& turns off

;side shift if it REACHES zero. Thus if ontime is always zero

;this is never executed - ie for continous operation

SIDEON	TST	ONTIME		is ontime zero

BEQ	RTNSON		Yes - then skip

DEC	ONTIME		No - decrement ontime

BNE	RTNSON		is ontime now zero?

BCLR	6,PORTB		Yes - turn off side shift

BCLR	7,PORTB

RTNSON	RTS

;{*******************************************************************}

;{###################################################################}

;SECONDS - heaps to do here - update & check timers for blade start,

;side start, side delay & check revs

SECONDS	LDA	#62

STA	SECS		Reset seconds counter 96 *16+ 2 +1 for zero

JSR	REVS		calculate revs & test for low revs

JSR	STARTER		count down starter times

JSR	SDELAY		count down side shift delay

RTS

;Get revs, display, update maxrevs, check for low revs

;turns led on when close to "low revs"

REVS	LDA	#$48		set display register ptr to posn for

STA	DPTR		Revs

LDA	REVCT		Get Rev count for 1s

CLR	REVCT		reset rev counter

ASL	A		double rev count (3 magnets * 2 = 1/10 rpm)

STA	REVCNT

LDX	REVCNT		revcount to index register - lowbyte

CLR	MR		clr high byte of number

LDA	#$03		convert num to 3 chrs

JSR	NUM_CHR

LDA	REVCNT		Get Rev Count

CMP	#140		Is it > 140? (*20 for rpm)

BHS	NMAXR		Yes - ignore count - goto Not Max Revs

CMP	MAXREV		No - Is Revcnt > MaxRev

BLS	NMAXR

STA	MAXREV		Yes - then MaxRevs = RevCnt

NMAXR	TST	BLADEST

BNE	RTNREVS		Skip revtest if starting

BRCLR	3,PORTB,RTNREVS	Skip revtest if off

LDA	MAXREV

CDM	SUB	#08		Is Revs < MaxRevs - 8(*20 for rpm)?

CMP	REVCNT

BHI	LEDON

BSET	0,PORTB		No - led off

BRA	RTNREVS

LEDON	BCLR	0,PORTB		Yes - led on

SUB	#04		If Revs < MaxRevs - 12 (*20 = 240rpm)

CMP	REVCNT

BLS	RTNREVS		no - then return

LDA	#$01

STA	PORTB		yes - turn machine off

LDA	#$59

STA	DPTR

LDA	#7

LDX	#LOREVS-#$0C00

LDA	#$0F

STA	LOCKED		Lock Machine

RTNREVS	RTS

;times down waterstart, blade start, side start

STARTER	TST	WATERST		If waterstart <>0 decrement

BEQ	BLSTRT		(disables lo volts test)

DEC	WATERST

BLSTRT	TST	BLADEST

BEQ	SIDEST		Is blade starting? No - onto side start timer

DEC	BLADEST		Yes - DEC blade start timer

BEQ	SIDEST		(disables lovlots, lo revs tests)

MTRST	LDA	#60

CMP	REVCNT		Are revs > (60 *20)

BHI	SIDEST		No - onto side start timer

CLR	BLADEST		Yes - then bladestart off

BSET	0,PORTB		Led off

SIDEST	TST	TSS		Is side shift starting?

BEQ	RTNSTR		No - RETURN

DEC	TSS		decrement Timer Side Start

BNE	RTNSTR		Has 3 secs of start? No - RETURN

BCLR	2,SIDE		Yes - side[start] = off

RTNSTR	RTS

;Side shift delay - count down seconds

SDELAY	TST	SIDE		Is machine side shifting?

BEQ	RTNDLY		No - skip lr delayer

BRCLR	5,MODE,RTNDLY	Is machine in grinder mode? - No - skip delay

BRSET	2,ENTRYM,RTNDLY	Is side shift by hold key -skip delay

TST	LRRATE		Is Rate = 0, then no delay

BEQ	RTNDLY

DEC	LRDELY		Decrement delay counter

BNE	RTNDLY		If not zero turn side off

LDA	LRRATE

STA	LRDELY

BRCLR	0,SIDE,LEFTT

BCLR	6,PORTB

BSET	7,PORTB

LDA	TLRON

STA	ONTIME

RTS

LEFTT	BCLR	7,PORTB

BSET	6,PORTB

LDA	TLRON

STA	ONTIME

RTNDLY	RTS

;Counts up timer, stops machine if timed out.

MINUTE	LDA	#60		Yes - reset minute timer

STA	MINCNT

BRCLR	4,PORTB,RTNMIN	Return if not countdown mode

INC	UPCNT		Increment upcount (timer counts up)

LDA	#$44		set display pointer to character position

STA	DPTR

CLR	MR		Clear high byte of number

LDX	UPCNT		Index Reg = upcnt, (low byte)

LDA	#$02		Convert number to two digits

JSR	NUM_CHR		and display

LDA	UPCNT

CMP	CNTDWN		does upcnt >= cntdwn?

BLO	RTNMIN		No - continue to SIDECNT

LDA	#$01		Yes - machine off

STA	PORTB

LDA	#$59

STA	DPTR

LDA	#7

LDX	#TIMOUT-#$0C00

JSR	DISPL

LDA	#$0F		Lock Machine

STA	LOCKED

RTNMIN	RTS

;Updates sidecount, if sideshift is happening

SIDECNT	TST	SIDE		This performed evey 10ms if machine unlocked

BEQ	RTNSID		Is side shift happening? No - return

LDA	PORTD		Read magnetic sensor

AND	#$80		= bit 8

CMP	OLDLR		Has there been a sensor change?

BEQ	STALLCK		No - Then better check for stall condition

STA	OLDLR		Yes - reset timer for stall check

CMP	#$80		Has sensor just turned on?

BEQ	SENSON		Yes - update l/r count

STALLCK	BRSET	6,PORTB,STALLC	execute stall check if Left or right

BRSET	7,PORTB,STALLC	side shifting

RTS

STALLC	INC	LRTIM		Got here only if sensor has not gone "on"

TST	TSS

BNE	RTNSID		so increment LRTimer; skip stall if starting

LDA	MINTIM		yes then :-

SUB	#03

CMP	LRTIM		is LRTim > MinTim - 3

BHS	RTNSID		Yes - then Led On

BCLR	0,PORTB		Led on - effect is to blink led near stall

LDA	MINTIM

CMP	LRTIM		If LRTime > MinTime

BHS	RTNSID

CLR	SIDE

LDA	#01

STA	PORTB		Stop machine

LDA	#$59

STA	DPTR

LDA	#7

LDX	#STALL-#$0C00

JSR	DISPL

LDA	#$0F

STA	LOCKED

JSR	INITKY

RTNSID	RTS

SENSON	CLR	LRTIM		sensor has just gone "on" - Clear LR timer

BSET	0,PORTB		Turn off led

TST	ENTRYM		Is entrymode = 0 (ie moving sideways by count)

BNE	RTNSID		NO - RETURN

TST	LRCNTL		Yes - then decrement LR counter

BNE	Z1		Does LRCNTL = 0? No - continue at Z1

DEC	LRCNTH		Decrement LRCNTH

Z1	DEC	LRCNTL		Decrement l/r counter low

LDA	LRCNTL

STA	TEMPL

LDA	LRCNTH		Divide LR Count by 2 for display

STA	TEMPH

LSR	TEMPH

ROR	TEMPL

LDA	TEMPH

STA	MR		Store LRCNTH / 2 in MR

LDA	#$56		Position character in display register

STA	DPTR

LDX	TEMPL		Index Reg = LRCNTL / 2

LDA	#$04		Convert number to 4 chacters

JSR	NUM_CHR		and place in display register

LDX	LRCNTL		Is LRCNTL = 0?

BNE	RTNSID		No - return

LDX	LRCNTH		Yes - Is LRCNTH =0?

BNE	RTNSID		No - return

CLR	SIDE		Yes - then side shift complete

BCLR	6,PORTB		Turn side shift off

BCLR	7,PORTB

BRCLR	5,MODE,NORML	Is Mode = grinder? No - then goto normal

LDA	#01		Yes - turn machine off

STA	PORTB

LDA	#$59

STA	DPTR

LDA	#7

LDX	#SHIFTD-#$0C00

JSR	DISPL

LDA	#$0F		Lock machine

STA	LOCKED

JSR	INITKY

RTS

NORML	BRCLR	3,PORTB,RTNSID	Is blade running? - No - return

WTRON	BRCLR	2,OLDW,RTNSID	Was the water on? - No - return

BSET	2,PORTB		yes - reinstate water

LDA	#2

STA	WATERST

CLR	OLDW

RTS

;Allows debounce time, checks for key being held on, gets new key

GETKEY	LDA	DEBNCE		DEBNCE = debounce time (5 * .01 secs)

BEQ	NNK		If debounce = 0 then get Next New Key

DEC	DEBNCE		Decrement debounce

RTS

NNK	JSR	SCANKBD		NextNewKey - scan keyboard

LDA	K		Key returned in K (0-F, 10 = nokey pressed)

CMP	OLDKEY		Is same key is still being held

BNE	NOTSAM		no - goto not the same key

SAMEK	BRCLR	5,MODE,SAMEKK	If mode = normal, check hold key

TST	SIDE

BEQ	SAMEKK		Mode grinder, not side shifting, check hold key

BRSET	2,ENTRYM,SAMEKK	grind,sideshift, and by holding #/* key

RTS

SAMEKK	LDA	K

CMP	#$0E		is key still "*"

BEQ	INCLR		yes - goto increment LR timer

CMP	#$0F		Is key still "#" - goto increment LR timer

BNE	INCNOK		No - goto inc LR not OK

INCLR	BRSET	2,ENTRYM,RTNSAM	If entrymode is already "hold" RETURN

INC	LRHOLD		Inc LR timer

LDA	LRHOLD

CMP	#20		Has * or # been held for 200ms?

BLO	RTNSAM		No - return

CLR	LRHOLD		Yes - clr LR timer,

LDA	#$04

STA	ENTRYM		and set entrymode - held(double)

LDA	#$05		reset debounce time

STA	DEBNCE

RTNSAM	RTS

INCNOK	BRCLR	2,ENTRYM,RTNSAM	Is entrymode = hold(double)	No - RETURN

INC	NOKHOLD		yes - then # nor * being held - so count up

LDA	NOKHOLD		nokey timer

CMP	#180		Has no key been pressed for 1.8s?

BLO	RTNSAM		No - return

CLR	NOKHOLD		Yes - reset nokey timer

BCLR	2,ENTRYM		reset entrymode[double] bit

LDA	ENTRYM

CMP	#$02		does entrymode = left

BNE	DISPR		No - goto right test

LDA	#'L		Yes - display "L" second line

BRA	AT50

DISPR	CMP	#$03		does entrymode = Right?

BNE	DISPSP		No - display a space

LDA	#'R		Yes - display 'R"

BRA	AT50

DISPSP	LDA	#'

AT50	STA	$50		Display the Character 1st pos, line 2

LDA	#$05

STA	DEBNCE		reset debounce timer

RTS

NOTSAM	CLR	LRHOLD		different key - LRHOLD is not being held

CLR	NOKHOLD		nor is "nokey" being (not)pushed

STA	OLDKEY		update oldkey

LDA	#05		reset debounce time

STA	DEBNCE

RTS

KEYS	LDA	#$05

CMP	DEBNCE		Has a key just been pressed?

BEQ	FRESHKY		Yes - goto fresh key

RTS

FRESHKY	LDA	LOCKED		Is machine locked?

BEQ	RUNKEY		No - Process keys for running machine

JSR	UNLOCK

RTS

RUNKEY	LDA	#$FC

AND	PORTB		IS machine running

BNE	RUNNING

TST	SIDE		or is machine side shifting

BEQ	KA		no - then "0" <> STOP goto key A

RUNNING LDA	K		YES - Then

CMP	#$00		If key = 0	then

BNE	KA

TST	ENTRYM

BNE	KA		if entrym = none then stop all

LDA	#$01

STA	PORTB		Turn off ALL

CLR	SIDE

LDA	#$0E		Stop all display updating

STA	LOCKED

LDA	#$59

STA	DPTR

LDA	#7

LDX	#STOPK-#$0C00

JSR	DISPL

JSR	INITKY

RTS

KA	LDA	K		Get the key

CMP	#$0A		If "A"

BNE	KB

JSR	AA

RTS

KB	CMP	#$0B

BNE	KC

JSR	B

RTS

KC	CMP	#$0C

BNE	KD

JSR	C

RTS

KD	CMP	#$0D

BNE	KE

JSR	D

RTS

KE	CMP	#$0E		"*"

BNE	KF

JSR	ASTER

RTS

KF	CMP	#$0F		"#"

BNE	NILK

JSR	HASH

RTS

NILK	CMP	#$10		No key depressed

BNE	DIGIT

JSR	NOKEY

RTS

DIGIT	LDA	ENTRYM		Key must be a digit.

BEQ	PREPRG		Does Entrymode = 0?

JMP	DOUBLE		No - try double

PREPRG	CLR	LOCKED		Yes - then preprogrammed side movement

BRCLR	4,PORTB,RCL1	Is mode = "countdown"?

JMP	DOUBLE		Yes - then not preprogrammed shift -goto dble

RCL1	LDA	K		CASE Key OF :-

CMP	#1		1

BNE	RCL2

LDA	LRLOLD			Repeat last distance left

STA	LRCNTL

LDA	LRHOLD

STA	LRCNTH

LDA	#$02

STA	ENTRYM			entrymode = "left"

JSR	D

RTS

RCL2	CMP	#2		2

BNE	RCL3

LDA	LRLOLD			repeat last distance right

STA	LRCNTL

LDA	LRHOLD

STA	LRCNTH

LDA	#$03

STA	ENTRYM

JSR	D

RTS

RCL3	CMP	#3		3

BNE	RCL4

CLR	SIDE

BCLR	6,PORTB			turn side shift off

BCLR	7,PORTB

BRCLR	0,MODE,RTNDIG		If machine is running

BRCLR	2,OLDW,RTNDIG		and water was on

BSET	2,PORTB			Restore water

LDA	#2			Water soleniod drags voltage low

STA	WATERST			So time water to disable Vtest

CLR	ENTRYM			clear entrymode

LDA	#' 			clear display

STA	$50

STA	$58

STA	$59

RTNDIG	RTS

RCL4	CMP	#4		4

BNE	RCL5

LDA	#100			move 50mm left

STA	LRCNTL

CLR	LRCNTH

LDA	#$02

STA	ENTRYM

JSR	D

RTS

RCL5	CMP	#5		5

BNE	RCL7

LDA	#100			move 50mm right

STA	LRCNTL

CLR	LRCNTH

LDA	#$03

STA	ENTRYM

JSR	D

RTS

RCL7	CMP	#$07		7

BNE	RCL8

LDA	#64

STA	LRCNTL

LDA	#1			move 160mm left

STA	LRCNTH

LDA	#$02

STA	ENTRYM

JSR	D

RTS

RCL8	CMP	#$08		8

BNE	RCL6

LDA	#64

STA	LRCNTL

LDA	#1			move 160mm right

STA	LRCNTH

LDA	#$03

STA	ENTRYM

JSR	D

RTS

RCL6	CMP	#6		6

BNE	RCL9

LDA	#12			move 8mm left

STA	LRCNTL

CLR	LRCNTH

LDA	#02

STA	ENTRYM

JSR	D

RTS

RCL9	CMP	#9		9

BEQ	RRCL9

CLR	ENTRYM			If not any digit -clear entrymode

JSR	IDLE

RRCL9	LDA	#12			move 8mm right

STA	LRCNTL

CLR	LRCNTH

LDA	#$03

STA	ENTRYM

JSR	D

RTS

DOUBLE	LDA	ENTRYM		Is entrymode = "double"?

CMP	#$04

BNE	NUMIN		No - then must be numeral entry

CLR	LOCKED

RTS

NUMIN	ASL	CNTL

ROL	CNTH

LDA	CNTL

LDX	CNTH

ASL	CNTL		Multiply current count by 10

ROL	CNTH		(10 = 8 + 2)

ASL	CNTL

ROL	CNTH

ADD	CNTL

STA	CNTL

STX	TEMPH

LDA	TEMPH

ADC	CNTH

STA	CNTH

LDA	K

ADD	CNTL		Add digit

STA	CNTL

LDA	#$0

ADC	CNTH

STA	CNTH

LDA	ENTRYM

CMP	#$01		Is entrymode timer?

BNE	LRNUM		No? try left or right

LDA	#$41		Yes - display count in timer part of display

STA	DPTR

LDA	#$02

CLR	MR

LDX	CNTL

JSR	NUM_CHR

LDA	CNTL

STA	CNTDWN

RTS

LRNUM	BRSET	1,ENTRYM,LRENTM

RTS

LRENTM	LDA	CNTH		If entrymode is Left or right

STA	LRCNTH

LDA	CNTL

STA	LRCNTL

ASL	LRCNTL

ROL	LRCNTH		LRcount = 2* Count

LDA	#$51		Display count

STA	DPTR

LDX	CNTL

LDA	CNTH

STA	MR

LDA	#$04		4 digits

JSR	NUM_CHR

RTS

;These key processors are all subroutines called by the above "keys" subroutine

AA	BRCLR	3,PORTB,MWON	Is Blade off? - No goto turn blade on

BCLR	2,PORTB		water off

BCLR	3,PORTB		blade off

BSET	0,PORTB		Led off

RTS

MWON	BSET	2,PORTB		water on

BSET	3,PORTB		blade on

BCLR	0,PORTB		Led on

LDA	#$03		3 seconds balde start timer

STA	BLADEST		disables lo revs, lo volts

LDA	#40		Set Maxrevs to 40 (*20 = 400rpm)

STA	MAXREV

LDA	#50		Set Max Volts to 50

STA	MAXV

LDA	ENTRYM		Does Entrymode = Timer?

CMP	#$01

BNE	RTNA		No - Idle

LDA	CNTL		Yes - then initiate timer

STA	CNTDWN

CLR	UPCNT

BSET	4,PORTB		reciprocate on

LDA	#$44		Set display register ptr

STA	DPTR

CLR	MR		clear high byte of number

LDX	UPCNT		ldx with number

LDA	#$02		convert and display 2 characters

JSR	NUM_CHR

CLR	ENTRYM		clear entrymode

RTNA	RTS

B	BRSET	2,PORTB,WOFF	If water is off turn it on

LDA	#2		Water soleniod drags voltage low

STA	WATERST		so use waterst to disable Vtest

BSET	2,PORTB

BSET	2,OLDW

RTS

WOFF	BCLR	2,PORTB

BCLR	2,OLDW

RTS

C	BRCLR	5,PORTB,GWON	Is Grinder off? - No goto turn grinder on

BCLR	5,PORTB		grinder off

BSET	0,PORTB		Led off

RTS

GWON

BSET	5,PORTB		aux on

BCLR	0,PORTB		Led on

RTS

D	LDA	ENTRYM

BEQ	RTND

ENTER	CMP	#$01		If entrymode = 1 (Timer)

BNE	LGO		Set timer going

LDA	CNTL		Store number in Cnt down.

STA	CNTDWN

CLR	UPCNT		Clear up counter

BSET	4,PORTB		reciprocate on

LDA	#$44		display upcount (0)

STA	DPTR

CLR	MR

LDX	UPCNT

LDA	#$02

JSR	NUM_CHR

CLR	ENTRYM		clr entry mode

RTND	RTS

LGO	CMP	#$02		If entrymode = Left Then

BNE	RGO		Go left

BCLR	0,SIDE		make sure right is off

BCLR	7,PORTB

BSET	1,SIDE		SIDE STATUS = LEFT

BSET	6,PORTB		LEFT ON

BRA	AGOGO		go

RGO	CMP	#$03		If entrymode = right

BNE	DBL		Go right

BCLR	1,SIDE		make sure left is off

BCLR	6,PORTB

BSET	0,SIDE		side status = right

BSET	7,PORTB		right on

AGOGO	BSET	2,SIDE		Side start status = true

LDA	LRCNTH		Save move distance

STA	LRHOLD

LDA	LRCNTL

STA	LRLOLD

BRCLR	5,MODE,NOTGL	Does operation mode = grinder? No - goto NotGL

BSET	2,PORTB		Water on

LDA	#2		Water soleniod drags voltage low

STA	WATERST		so use waterst to disable Vtest

LDA	LRRATE

STA	LRDELY

BEQ	NOERR

BCLR	7,PORTB

BCLR	6,PORTB

BRA	NOERR		Skip slop/blade thickness adjustments

NOTGL	LDA	PORTB

AND	#$04		Save water status

STA	OLDW

BCLR	2,PORTB		turn off water

LDA	LRCNTH		If distance > 128mm

CMP	#$01

BLO	LRGO

BCLR	3,PORTB		blade off

BCLR	4,PORTB		reciprocate off

LRGO	LDA	#03

ADD	LRCNTL		add 3 (1.5mm) to count - blade thickness

STA	LRCNTL

LDA	#0

ADC	LRCNTH

STA	LRCNTH

NOERR	LDA	ENTRYM		conserve entrymode

STA	OLDEM

CLR	ENTRYM		clear enrtry mode

LDA	#$51

STA	DPTR		display LR counts

JSR	LRCNTDP

LDA	#2

STA	TSS

RTS

DBL	CLR	ENTRYM		If entrymode was none of above, must be double

LDA	#'

STA	$50		Clear entrymode & display

RTS

;End of "D"		{.......}

ASTER	BRCLR	2,ENTRYM,EMLEFT	Is entrymode = double? No - GoTo Entrymod left

LDA	#'H		Yes - display "H" for hold

STA	$50

BRCLR	2,PORTB,NOWATRL	store water status

BSET	2,OLDW

NOWATRL BRSET	5,MODE,NOTWL	Is mode = grinder? Yes then skip wateroff

BCLR	2,PORTB		Turn water off

NOTWL	BCLR	7,PORTB		Make sure right is off

BSET	6,PORTB		Move Left

LDA	#2

STA	TSS		side start timer = 2

LDA	#$06

STA	SIDE		set start, left status on, Right off

LDA	#02		set old EM as "left"

STA	OLDEM

RTS

EMLEFT	LDA	SIDE		Entrymode must be l/r! Has side move commenced?

BEQ	EMLEFT1		No - GO set entrymode to "left"

RTS

EMLEFT1 LDA	#$02		Set entrymode to left

STA	ENTRYM

LDA	#'L		Display "L"

STA	$50

CLR	CNTL		Clear counter

CLR	CNTH

LDA	#$51

STA	DPTR

CLR	MR

LDX	CNTL

LDA	#$04		display 4 zeros

JSR	NUM_CHR

RTS

;End of "*"			{.......}

HASH	BRCLR	2,ENTRYM,EMRIGH	Is entrymode = double? No - Goto Entrymde Right

LDA	#'H		Yes - display "H" for hold

STA	$50

BRCLR	2,PORTB,NOWATRR	Store water status if water on

BSET	2,OLDW

NOWATRR BRSET	5,MODE,NOTWR	Is mode = grinder? Yes then skip wateroff

BCLR	2,PORTB

NOTWR	BCLR	6,PORTB		Make sure Left is off

BSET	7,PORTB		Right on

LDA	#2

STA	TSS		side start timer = 2

LDA	#$05

STA	SIDE		Set start, right status on, left off

LDA	#03		Set OldEM as "right"

STA	OLDEM

RTS

EMRIGH	LDA	SIDE		Entrymde must be l/r! Has side move commenced?

BEQ	EMRGHT1		No - go set entrymode to "right"

RTS

EMRGHT1 LDA	#$03		Set entrymode to "Right"

STA	ENTRYM

LDA	#'R		Display "R"

STA	$50

CLR	CNTL		Clear counter

CLR	CNTH

LDA	#$51

STA	DPTR

CLR	MR

LDX	CNTL

LDA	#$04		display 4 zeros

JSR	NUM_CHR

RTS

;End of "#"			{.......}

NOKEY	LDA	ENTRYM		Is entrymode = double?

CMP	#$04

BEQ	STPSIDE		NO - Then return

RTS

STPSIDE BCLR	6,PORTB		Yes - stop side shift

BCLR	7,PORTB

CLR	SIDE

BRCLR	3,PORTB,RTNNOK	If machine is running

BRCLR	2,OLDW,RTNNOK	If water was on restore water

LDA	#2		Water soleniod drags voltage low

STA	WATERST		so use waterst to disable Vtest

BSET	2,PORTB

CLR	OLDW		clear old water status

RTNNOK	RTS

LRCNTDP LDA	LRCNTL		This subroutine

STA	TEMPL		divides the LRcount by 2

LDA	LRCNTH

STA	TEMPH

LSR	TEMPH

ROR	TEMPL		for DISPLAY

LDA	TEMPH

STA	MR

LDX	TEMPL

LDA	#$04

JSR	NUM_CHR		Convert number to chars and display

RTS

;{***********************************************************************}

;{#######################################################################}

UNLOCK	LDA	LOCKED

CMP	#$0F		Has first PIN number been entered?

BEQ	FIRSTK		yes - go to FIRST KEY

CMP	#$0E

BEQ	SECNDK

CMP	#$0D

BEQ	THIRDK

CMP	#$0C

BEQ	JMPFRTH

CMP	#$0B

BEQ	JMPFTH

WRONGK	LDA	K

CMP	#$10

BEQ	RTNUNL

LDA	#$0F

STA	LOCKED

RTNUNL	RTS

JMPFRTH	JMP	FORTHK

JMPFTH	JMP	FIFTHK

FIRSTK 	LDA	K		No - get key

CMP	#$02		Key = "2"?

BEQ	TWOO		Yes - decrement lock

JSR	DISPDAT

RTS

TWOO	CLI

DEC	LOCKED

JSR	INITAL

LDX	#$40

STX	DPTR

JSR	CLRDP

LDA	#26

LDX	#DONTAGN-#$0C00

JSR	DISPL

RTS

SECNDK	LDA	K

CMP	#$02

BNE	WRONGK

DEC	LOCKED

LDA	#$40

STA	DPTR

LDA	#27

LDX	#IN789-#$0C00

JSR	DISPL

RTS

THIRDK	LDA	K

CMP	#$07		Key = "7"  mode = norm

BNE	NINE		No - try nine

BCLR	5,MODE

JSR	INITDP

LDA	#$5B

STA	DPTR

LDA	#5

LDX	#NMAL-#$0C00

JSR	DISPL

CLR	LOCKED

RTS

NINE	CMP	#$09

BNE	EIGHT

BSET	5,MODE

LDX	#$40

STX	DPTR

JSR	CLRDP

LDA	#16

LDX	#INPTDLY-#$0C00

JSR	DISPL

DEC	LOCKED

RTS

EIGHT	CMP	#$08

BEQ	EIGHT1

JMP	WRONGK

EIGHT1	CLR	LOCKED

BCLR	5,MODE

JSR	INITDP

LDA	#$5B

STA	DPTR

LDA	#5

LDX	#TIMER-#$0C00

JSR	DISPL

BSET	0,ENTRYM		Enter timer entry mode

CLR	CNTL		Clear counts

CLR	CNTH

LDA	#$41		Display count (ie 0)

STA	DPTR		position

CLR	MR		high byte

LDX	CNTL		low byte

LDA	#$02		num of chrs

JSR	NUM_CHR

RTS

;End of third key

FORTHK	LDA	K

CMP	#$10

BEQ	RTN4

STA	LRRATE

LSL	LRRATE

BEQ	INI5

LDA	#$40

STA	DPTR

LDA	#23

LDX	#INPTON-#$0C00

JSR	DISPL

DEC	LOCKED

RTN4	RTS

FIFTHK	LDA	K

CMP	#$10

BEQ	RTN5

STA	TLRON

LSL	TLRON

LSL	TLRON

LSL	TLRON

INI5	JSR	INITDP

LDA	#$5B

STA	DPTR

LDA	#5

LDX	#GRIND-#$0C00

JSR	DISPL

CLR	LOCKED

RTN5	RTS

;{******************************************************************}

;{###################################################################}

INITKY	LDA	#$40

STA	DPTR

LDA	#16

LDX	#DONT2-#$0C00

JSR	DISPL

RTS

INITDP	LDX	#$40

JSR	CLRDP

LDA	#'T

STA	$40

LDA	#'R

STA	$47

LDA	#'V

STA	$4C

LDA	#'-

STA	$43

STA	$55

RTS

CLRDP	LDA	#'

NEXT	STA	,X

INCX

CPX	#$60

BNE	NEXT

RTS

DISPDAT LDX	#$40		This subroutine displays various data

STX	DPTR

JSR	CLRDP

LDA	#16

LDX	#MAXES-#$0C00

JSR	DISPL

LDA	#$50

STA	DPTR

LDX	MINIDL

CLR	MR

LDA	#03

JSR	NUM_CHR

LDA	#$56

STA	DPTR

LDX	MAXV

CLR	MR

LDA	#03

JSR	NUM_CHR

LDA	#$5C

STA	DPTR

LDX	MAXREV

CLR	MR

LDA	#03

JSR	NUM_CHR

RTS

LCD	INC	LCDPTR		This subroutine displays the next character

LDX	LCDPTR		in sequenece

CPX	#$50		If finished topline, set cursor to

BNE	EOL2

BCLR	0,PORTA

LDA	#$C0

STA	PORTC		first position, second line

BSET	1,PORTA

BCLR	1,PORTA

JSR	DELAY

EOL2	CPX	#$60		Is it at end of second line?

BNE	NEXTCHR		No - display nect chr

LDX	#$40		If finished second line, place cursor

STX	LCDPTR

BCLR	0,PORTA		"home"

LDA	#$80

STA	PORTC

BSET	1,PORTA

BCLR	1,PORTA

JSR	DELAY

NEXTCHR LDX	LCDPTR		sends the next character in the display

BSET	0,PORTA		register to the display

LDA	,X

STA	PORTC

BSET	1,PORTA

BCLR	1,PORTA

RTS

SCANKBD LDA	#$E0			Scan Keyboard

STA	PORTC

BRSET	2,PORTA,L100

LDA	#$01

STA	K

RTS

L100	BRSET	3,PORTA,L101

LDA	#$02

STA	K

RTS

L101	BRSET	4,PORTA,L102

LDA	#$03

STA	K

RTS

L102	BRSET	5,PORTA,L103

LDA	#$0A

STA	K

RTS

L103	LDA	#$D0

STA	PORTC

BRSET	2,PORTA,L104

LDA	#$04

STA	K

RTS

L104	BRSET	3,PORTA,L105

LDA	#$05

STA	K

RTS

L105	BRSET	4,PORTA,L106

LDA	#$06

STA	K

RTS

L106	BRSET	5,PORTA,L107

LDA	#$0B

STA	K

RTS

L107	LDA	#$B0

STA	PORTC

BRSET	2,PORTA,L108

LDA	#$07

STA	K

RTS

L108	BRSET	3,PORTA,L109

LDA	#$08

STA	K

RTS

L109	BRSET	4,PORTA,L110

LDA	#$09

STA	K

RTS

L110	BRSET	5,PORTA,L111

LDA	#$0C

STA	K

RTS

L111	LDA	#$70

STA	PORTC

BRSET	2,PORTA,L112

LDA	#$0E

STA	K

RTS

L112	BRSET	3,PORTA,L113

LDA	#$00

STA	K

RTS

L113	BRSET	4,PORTA,L114

LDA	#$0F

STA	K

RTS

L114	BRSET	5,PORTA,L115

LDA	#$0D

STA	K

RTS

L115	LDA	#$10

STA	K

RTS

DISPL	STA	CC

DISPL1	LDA	$0C00,X

INCX

STX	MR

LDX	DPTR

STA	,X

INCX

STX	DPTR

LDX	MR

DEC	CC

BNE	DISPL1

RTS

DELAY	LDA	#$2F

LOOPDEL DEC	A

BNE	LOOPDEL

RTS

NUM_CHR STA	CC		A contains the character count

STX	NUML		X contains low byte

STX	TEMPL

LDA	MR		MR contains high byte

STA	NUMH

STA	TEMPH

LDA	CC

CMP	#$04

BNE	HUNDRD

CLRX

LP1000	LDA	TEMPL

SUB	#232		232 + 3*256 = 1000

STA	TEMPL

LDA	TEMPH

SBC	#03

STA	TEMPH

BMI	OT1000		If minus donot increment thousands counter

STA	NUMH

LDA	TEMPL		Store result of subtraction of 1000

STA	NUML

INCX

BRA	LP1000		loop back

OT1000	TXA

ADD	#$30		get thousands count - add chr(0)

LDX	DPTR		and display

STA	,X

INC	DPTR		increment display ptr

HUNDRD	LDA	NUML

STA	TEMPL

LDA	NUMH

STA	TEMPH

CLRX

LDA	CC

CMP	#$03

BMI	TEN

LOOP100	LDA	TEMPL

SUB	#100

STA	TEMPL

LDA	TEMPH

SBC	#0

STA	TEMPH

BMI	OUT100

STA	NUMH

LDA	TEMPL

STA	NUML

INCX

BRA	LOOP100

OUT100	TXA

ADD	#$30			add character "0"

LDX	DPTR

STA	,X

INC	DPTR

TEN	LDA	NUML

STA	TEMPL

CLRX

LOOP10	LDA	TEMPL

SUB	#10

STA	TEMPL

BMI	OUT10

STA	NUML

INCX

BRA	LOOP10

OUT10	TXA

ADD	#$30			add character "0"

LDX	DPTR

STA	,X

INC	DPTR

LDA	NUML

ADD	#$30			add character "0"

LDX	DPTR

STA	,X

RTS

INITAL	SEI

LDA	#$FF

STA	DDRB		Port B all output

LDA	#127

STA	MINIDL		Minimum idle count = 127

LDA	#$03

STA	DDRA		Port A, input except bits 0,1

CLR	PORTA			All devices off

LDA	#$01

STA	PORTB

LDA	#$FF		PortC all output

STA	DDRC

LDA	#0

STA	PORTC

LDA	#62			100 cnts = 1 sec

STA	SECS

LDA	#60

STA	MINCNT		60 seconds = 1 minute

LDA	#140

STA	MAXREV		Maximum revs set to 1400rpm

LDA	#$5F		LCD point to last chr of 2nd line

STA	LCDPTR		Actually points to display register

LDA	#$10

STA	OLDKEY		Oldkey = "nokey"

LDA	#$04

STA	DEBNCE		Debounce time = 40ms

LDA	#$20		Clear mode except run mode

AND	MODE

STA	MODE

CLR	CHRD

LDA	#20

STA	MINTIM		Minimum side time = 200ms

CLR	MRI2		Clear hardware interupt

LDA	#$10

STA	K

CLR	LRTIM		LRTimer

CLR	OLDLR		Old LR Timer

CLR	SIDE

CLR	TSS

BSET	2,BLADEST	blade start time = 4 secs - no voltage mesured

BSET	2,TSS		Side start = 4 secs - no stall checked

LDA	#10

STA	MAXV

CLR	MSGPTR

CLR	MSGPTR2

CLR	ENTRYM

LDX	#$40

LDA	#'

CLEARL	STA	,X

INCX

CPX	#$59

BNE	CLEARL

LDA	#$38			Set DISPLAY 2 lines, 8bit, 5x7

STA	PORTC

BSET	1,PORTA

JSR	DELAY

BCLR	1,PORTA

LDX	#60

MSDEL	JSR	DELAY

JSR	DELAY

JSR	DELAY

JSR	DELAY

JSR	DELAY

JSR	DELAY

JSR	DELAY

JSR	DELAY

JSR	DELAY

JSR	DELAY

JSR	DELAY

JSR	DELAY

JSR	DELAY

DECX

BNE	MSDEL

LDA	#$38

STA	PORTC

BSET	1,PORTA

BCLR	1,PORTA

JSR	DELAY

JSR	DELAY

JSR	DELAY

JSR	DELAY

JSR	DELAY

JSR	DELAY

LDA	#$38

STA	PORTC

BSET	1,PORTA

BCLR	1,PORTA

JSR	DELAY

LDA	#$38

STA	PORTC

BSET	1,PORTA

BCLR	1,PORTA

JSR	DELAY

LDA	#$38

STA	PORTC

JSR	DELAY

BSET	1,PORTA

JSR	DELAY

BCLR	1,PORTA

JSR	DELAY

LDA	#$0C			DISPLAY on, cursor blink off

STA	PORTC

JSR	DELAY

BSET	1,PORTA

JSR	DELAY

BCLR	1,PORTA

JSR	DELAY

LDA	#$06			screen station, cursor move right

STA	PORTC

JSR	DELAY

BSET	1,PORTA

JSR	DELAY

BCLR	1,PORTA

JSR	DELAY

LDA	#$01

STA	PORTC

JSR	DELAY

BSET	1,PORTA

JSR	DELAY

BCLR	1,PORTA

JSR	DELAY

LDA	#$02

STA	PORTC

JSR	DELAY

BSET	1,PORTA

JSR	DELAY

BCLR	1,PORTA

JSR	DELAY

LDA	#$80			cursor to home

STA	PORTC

JSR	DELAY

BSET	1,PORTA

JSR	DELAY

BCLR	1,PORTA

JSR	DELAY

LDA	#$4F

STA	TIMCTL

LDA	#126			78 * 7-bit prescale = 0.01 sec

STA	TIMDAT

CLR	LRDELY

CLI

RTS

ORG	$0C00

STOPBR	FCC	"Stopbar"			;7

GRIND	FCC	"Grind"				;5

LOVOLT	FCC	"LoVolts"			;7

LOREVS	FCC	"Lo Revs"			;7

TIMER	FCC	"Timer"				;5

TIMOUT	FCC	"TimeOut"			;7

DONTAGN	FCC	"Don't do that        again"	;26

IN789	FCC	"7-Norml 8-Timer   9-Grinder"	;27

NMAL	FCC	"Norml"				;5

INPTON	FCC	"Input ON Time  	  *80ms"		;23

INPTDLY	FCC	"Input Delay *2s "		;16

SHIFTD	FCC	"Shifted"			;7

STALL	FCC	"Stalled"			;7

STOPK	FCC	"Stopkey"			;7

DONT2	FCC	"Don't Press 2   "		;16

MAXES	FCC	"Idle MaxV MaxREV"		;16